## Slide 1: Retail Competition, Open Access, Power Markets and DISCOMs A medium-term outlook
Ann Josey
Prayas (Energy Group)
Distribution Utility Meet (DUM 2017)
29th November 2017, Bangalore

## Slide 2: About Prayas (Energy Group)
Energy (Policy, Planning & Governance)
Electricity Regulation
Rural Energy
Renewable Energy
Fossil fuels governance
Energy and Resources
Energy Efficiency
Not-for-profit organisation founded in 1994
Analysis based policy advocacy for promoting public interest
  Focus on governance aspects & policy innovation
  Part of several high-level Govt. Committees & regulatory processes
  Regulatory commissions: Consumer Representative before MERC and CERC, Advisory Committees of CERC and 5 SERCs
  NITI Aayog: 175 GW Expert Committee, Low Carbon Inclusive Growth, India Energy Security Scenarios, New Integrated Energy Policy; Indo-US energy dialogue.
  MoP and MNRE: RE Law, 12th Plan and Tariff Rationalisation Committee

## Slide 3: Utility Business Model at cross roads
Significant sales migration via open access, captive and rooftop solar
Alternative options competitive for large consumers
  Average cost of supply already > Rs. 6.5/kWh for some DISCOMs
  Energy charges @ Rs. 7- 8/kWh for cross-subsiding consumers
Technological and Market Structure changes
  Falling RE prices and rising costs of thermal power
  Advent of storage
  Increasing trades in power exchanges, bilateral market
  Rise of consultancy services to facilitate/aggregate procurement solutions.

## Slide 4: Significant Sales Migration in the recent past..1
Note: Estimates for Rajasthan for FY 16. Estimates for Madhya Pradesh from Sept ’15 to Aug’16.
Source: PEG compilation from regulatory orders and petitions based on estimates or actual sales reported by DISCOMs
Open Access
Extent of Open Access in 2016-17 (MUs)
Open access power purchase through PXs : ~ 24,000 MUs in FY 17.
  Accounts for more than 60% of the trade on power exchanges
  Most of the trade from Tamil Nadu, Andhra Pradesh, Gujarat and Haryana
Open Access has also been growing in many states in the recent past:
  Rajasthan: 74% ↑ (FY 15- FY 16)
  Karnataka: 105% ↑ (FY 16 - FY 17)
  Gujarat: 16% ↑ (FY 16 - FY 17), despite levy of additional surcharge
  Maharashtra: 29% ↑ (FY 16 - FY 17)
Chart: Open Access (MUs)
| Maharashtra | Gujarat | Rajasthan | Karnataka | Haryana | Andhra Pradesh | Punjab | Madhya Pradesh
Open Access (MUs) | 6348 | 4375 | 5281 | 2314.721 | 2204.7 | 2069 | 1916.08 | 531.7
% of HT sales | 0.21339 | 0.18892 | 0.22442 | 0.17158 | 0.15855 | 0.12307 | 0.13518 | 0.040585

## Slide 5: Significant Sales Migration in the recent past..2
Captive
Steady 4% increase in captive consumption in the past three years
Between FY 14 and FY 15, 9% ↑ in Odisha, 12%↑ in Chattisgarh and 34% ↑ in Karnataka
Consumption patterns change across years in states which adds to uncertainty.
Roof-top solar
1345 MW is estimated capacity till September 2017.
Another 1500 MW expected to be added in the next year itself.
Tamil Nadu, Karnataka, Maharashtra, Gujarat have the highest penetration
Competitive prices and rising DISCOM tariffs will further increase penetration
Chart: Consumption by CPP with capacity > 1MW
| Gujarat | Odisha | Tamil nadu | Chattisgarh | Karnataka | Uttar Pradesh | Rajasthan | Maharashtra | Jharkhand | Madhya Pradesh | West Bengal | Punjab | Kerala | Uttarakhand | Haryana | Assam
FY 13 | 27184.55 | 24466.76 | 14300.11 | 13877.79 | 11881.92 | 12032.17 | 9552.1 | 12291.57 | 9005.27 | 7021.68 | 5494.34 | 3203.55 | 1867.48 | 3026.89 | 1608.15 | 1282.53
FY 14 | 28582.25 | 24983.22 | 16238.14 | 14364.3 | 12548.93 | 11812.28 | 11184.75 | 12794.34 | 9177.64 | 7532.08 | 5312.23 | 3600.89 | 1840.34 | 2136.37 | 1690.13 | 1328.2
FY 15 | 29148.11 | 26681.08 | 19651.65 | 18778.66 | 16439.77 | 11686.07 | 11351.97 | 10389.47 | 9118.1 | 7011.53 | 5993.22 | 4166.12 | 2200.48 | 2167.1 | 1843.61 | 1338.13
Captive generation as a % of total consumption | 0.30099 | 0.67395 | 0.2261 | 0.53935 | 0.24325 | 0.15603 | 0.19618 | 0.091425 | 0.41163 | 0.15193 | 0.14507 | 0.10065 | 0.11191 | 0.19787 | 0.055709 | 0.19964
Captive consumption (MUs) , relative % to DISCOM sales
Source: CEA

## Slide 6: Tariff for large consumers > competitive rates
About 60% to 70% of non- agricultural sales higher than Rs.5/unit .
This is comparable to indicative rooftop-solar prices.
The eligible sales will increase in coming years with increasing ACoS, tariffs of DISCOMs.
DISCOMs will have small consumer demand to service.
Storage options will further sales migration.
Source: Various tariff orders

## Slide 7: Short-term Open Access (STOA)
More than 100% variation in monthly open access quantum across states within a year.
Significant diurnal variation in some states
Power procurement planning less challenging if consumers go for good.
  Increases certainty in demand
  Opens up avenues to manage surplus
Possibility of year-long open access contracts?
Need for market instruments to cater to longer term open access?
For Distribution Open Access, DISCOMs submit combined schedules to SLDCs
  DISCOM+ embedded OA consumers
Cost of deviation due to open access borne by DISCOM
  penalties for overdrawal, load shedding
Need for equitable, transparent mechanism for deviation settlement for embedded open access consumers
  Basis for sharing costs for deviation?
  Methodology used for aggregation and revision of schedules?
  Allowing higher deviation for RE power?
Majority of open access in India is short-term
  60% of Day-Ahead Market trade in Power Exchanges due to Open Access
Pose Challenges with :
Power Procurement Planning
Scheduling

## Slide 8: Renewable Energy Open Access: Increasing competitiveness
Chart: Rs./kWh
| Gujarat | Maharashtra | Rajasthan | Tamil Nadu
Cost of Power | 3.5 | 3.5 | 3.5 | 3.5
Cost of Power | 3.5 | 3.5 | 3.5 | 3.5
Wheeling and Transmission Losses | 0.54461 | 0.37532 | 0.28551 | 0.23002
Wheeling and Transmission Losses | 0.54461 | 0.37532 | 0.28551 | 0.23002
Wheeling and Transmission Charges | 0.5399 | 0.85974 | 0.43871 | 0.35076
Wheeling and Transmission Charges | 0.5399 | 0.85974 | 0.43871 | 0.1403
CSS | 1.44 | 1.65 | 1.39 | 1.67
CSS | 0.72 | 1.65 | 0 | 0.835
Additional Surcharge | 0.305 | 1.24 | 0.8 | 0
Additional Surcharge | 0.61 | 1.24 | 0.8 | 0
RPO Cost | 0.1 | 0.125 | 0.114 | 0.14
RPO Cost | 0 | 0 | 0 | 0
Increasing viability of renewable energy (RE) based open access
  Cheaper than coal if base price for both RE and coal assumed @ Rs. 3.5/unit.
  This is due to concessions for RE open access
Need to re-evaluate RE related concession in states.
  Loss of revenue due to concessions being borne by DISCOM/consumers- evaluate support options
  Significant impact in RE-rich states
    Andhra Pradesh: Removal of concessions for RE-based open access generates as much revenue as levying an additional surcharge of Rs. 1/kWh on all open access consumers.
Coal | Wind |  | Coal | Wind |  | Coal | Wind |  | Coal | Wind
Gujarat |  |  | Maharashtra |  |  | Rajasthan |  |  | Tamil Nadu | 
Source: Various regulatory orders
Data for 2017-18

## Slide 9: Renewable Energy Open Access: Banking
Variation between infirm generation from RE sources, open access load absorbed by DISCOM
  Needed due to seasonal, diurnal variations, low CUF, mismatch of generation and load in real time
  Generation in excess of demand can be banked and later unbanked
Characteristics of Banking services
  Charges: usually , 2% of banked energy , Buy-back period: mostly one year
DISCOMs incurs cost due to service especially due to difference in cost of power at the time of injection and drawal of banked energy
  Difference passed on to the non-open access consumers of DISCOM
MSEDCL’s proposal to compensate DISCOM for banking services
  Settlement and valuation linked to Merit Order Dispatch and marginal cost incurred by DISCOM
  Value of banked energy at time of injection  lowest variable cost of backed down power
  Value of banked energy at time of drawal  highest variable cost of dispatched power (incl.PXs)
  Estimations to take place on a 15 minute block basis with monthly settlement
  Proposal will ↑ banking charge from Rs.0.06/kWh to Rs.0.28/kWh landed price inc, only 3%
  Impact will vary from DISCOM to DISCOM

## Slide 10: Sales Migration charges…1
Uncertainty in CSS, Wheeling charges
  Changes on a year on year basis
    Maharashtra (FY 11 to FY 18): +100% to -50% in CSS, +175% to -40% in wheeling
    Gujarat (FY 11 to FY 18) : +150% to – 40% in CSS, +10% to -1% in wheeling
  Changes the viability of open access, encourages opportunistic switching
  Can think of a fixed trajectory for wheeling and CSS charges over a 5 year period?
    Per unit CSS (Rs/kWh) fixed thus reducing real rates over time
    Wheeling charge trajectory  fixed with incentives for efficiency improvement
Additional surcharge estimation
  Typically estimated on the basis of overall average fixed cost of power
  Could lead to under-estimation/over-estimation
    Under-estimation : If new plants with high fixed cost being backed down.
    Over-estimation : with depreciated or gas-based plants being backed down.
  Ideally, it should reflect cost of backing down –i.e: the average fixed cost of the plants backed down due to open access

## Slide 11: Sales Migration charges..2
Standby charges estimation
  Some states use mutually agreed rates with consumer- practice not preferred.
  Given the risk of load shedding for low paying DISCOM consumers, open access consumers should be encouraged to find other standby options.
    Should standby power be provided at prohibitive rates (1.5 times applicable tariff) like in some states?
    Should standby power till a certain level (say, 20% of contracted demand) be provided at nominal rates to encourage open access?
Sales migration charges cannot address loss of revenue
  Cross-subsidy levels are much higher than the 20% of ACoS
  With surplus power, several states levying additional surcharges
    Open access  10% to 25% of backing down
  ACoS high and ↑- cost competitiveness unlikely with efficiency improvements.
  High sales migration charges can incentivise consumers migration to captive.

## Slide 12: DISCOM Strategy: Reducing ABR for HT consumers
Time of Day (ToD) tariff in Maharashtra
  Source : MERC order in Case 48 of 2016
  Open Access is high in off-peak times even with a tariff rebate of Rs.1.50 per unit.
  In fact, off-peak open access comparable to Peak open access despite peak tariffs
  Power available at PXs at Rs.2.19/kWh during off-peak hours.
Industrial consumer tariff reduction
ToD time slot | Time Slot | ToD Tariff (Rs./kWh) | Open Access as % of open access in A
6:00-9:00 | A: Other than peak, off-peak | 0 | 726
12:00 to 18:00 |  |  | 
9:00 to 12:00 | B: Peak | 0.8 | 728
18:00 to 22:00 |  | 1.1 | 729
22:00 to 6:00 | C: Off-peak | -1.5 | 731
Punjab
FY 16 - FY 17:2% ↓ in energy charges
Maharashtra
FY 15- FY 16: Subsidy for HT consumers reduced tariff by about 16%
In same period, open access ↑ by 29%
FY 17 : New industries charged subsidised tariff of Rs. 4.99/kWh
In same period, open access ↓ by only 46 MUs (2%)

## Slide 13: Other strategies
Increasing revenue from captive sales
  Parallel operation charges in Gujarat and Tamil Nadu for grid support services
Levy of electricity duty
  On all users of the grid including captive consumers
  Revenue used to support loss making DISCOMs
Change cross-subsidy model
  Increase in intra-category cross- subsidy
Reduce average cost of supply
  Increase in generation efficiency
  Reduction in T&D losses
  Rationalisation of coal costs
  At most these measures will slow the rate of increase of ACoS in many states
Many of these measures might slow sales migration
  Provide short-term relief: At most it will buy a year or two for the DISCOM
  Falling prices and storage options will change the market

## Slide 14: Observations…1
Sales migration is an inevitability
  Will take place even without the introduction of multiple supply licensees as envisages in E-Act Amendment
  Cheaper alternatives and increasing cost of supply major factors
  Tweaks in tariff design at most brings short-term relief
DISCOM Business Model needs to change
  Provider of wires and supply  Provider of wires
  Universal supply obligation  Supplier of last resort
  Dominant grid user  Grid Balancing
  Catering to state demand  Catering to demand of small consumers (LT domestic, agriculture)
  Cross subsidy based model  Cost of supply/ Subsidy model, Possibility of other revenue streams
Need to prepare for the transition in DISCOM business
  Demand uncertainty: Assessment needs to include impact of sales migration
  Power procurement: Rethink flexibility, Duration of PPAs

## Slide 15: Observation …2
Market operations fundamental to transition
  Need to move towards capacity markets
  Facilitate utilisation of stranded capacity, backed down power
  More flexibility in terms of contracts, instruments
Is the Indian power market ready?
  Lack of flexible longer-term market instruments in PXs, traders
  Fragmentation in markets
    different players, prices, lack of information, varied instruments
  Regulation of new players?
  Need for analysis based reports at state level
    Similar to CERC Market Monitoring reports
Need for increasing institutional capacity during transition
  LDCs, DISCOMs: to plan operations given uncertain demand, supply and provide grid services
  SERCs : to ensure robust market operations, protect interest of small consumers
  PXs, Traders, Generators: To provide innovative market instruments to optimise assets and increase flexibility.

## Slide 16: Thank you
ann@prayaspune.org
shantanu@prayaspune.org